## Slide 1: Design of Digital Circuits Lab 9 Supplement: The Performance of MIPS
Prof. Onur Mutlu
ETH Zurich
Spring 2019
14 May 2019

## Slide 2: This is the Last Lab
You still have one more lab session to show your work to the TAs. You do not need to attend these sessions if you do not want to show anything.
  Tuesday, May 21th
  Wednesday, May 29rd
  Friday, May 31st

## Slide 3: What we have done so far
You have learned how gates work and how to build small modules out of them.
You combined those modules into more powerful ones.
You learned how to test code via simulation and test benches.
You learned how to write MIPS assembly code.
And finally: You combined all of that knowledge to build a simple processor and even ran your own programs on it.

## Slide 4: Lab 9 Overview
Extend the processor from the previous lab: srl, mflo, multu
Measure the performance of the processor.

## Slide 5: Lab 9: New Instructions
The processor can already add and subtract but to be able to efficiently compute we want to add multiplication.
By shifting we can multiply and divide by powers of 2.
You are only required to implement a logic right shift (srl)
  but feel free to implement a arithmetic right shift and logic left shift.
Every left shift can be implemented by a normal multiplication so we don’t need it.

## Slide 6: Lab 9: How to do 32-Bit Multiplication
The result of a multiplication of two 32-bit numbers can have up to 64 bits.
Two stage approach:
  MIPS has special registers (Hi and Lo) where the upper 32 bits of the multiplication result are saved in Hi and the lower 32 ones in Lo (no output from the ALU.)
  mfhi and mflo can then retrieve the values.

## Slide 7: Lab 9: Performance
We want to determine the performance of our processor on the example that you implemented in Lab 7: summing up numbers:
  Once with a loop that performs back to back additions.
  Once with the Gaussian formula that performs multiplication.
You can use your implementation from Lab 7 and write a new code for calculating the Gaussian formula or use the code that we provide.
Finally, you will test your processor with a test bench.

## Slide 8: Returning FPGAs
Ideally you all should return the boards during your last lab session, but if necessary you still can keep using it until June 18th.
Hand it over to your TA during the lab session or bring it to D77, E78 or F72.

## Slide 9: Last Words
In this lab, you will add instructions to the processor.
  Adding instructions improves the processor design.
  But this comes at a cost: more instructions have to be decoded and more hardware resources are required.
Processor designers need to face these trade-offs.
We hope you have enjoyed the labs.
  You have implemented your own 32-bit processor.
  You have written programs for it.
  You have improved its performance.

## Slide 10: Design of Digital Circuits Lab 9 Supplement: The Performance of MIPS
Prof. Onur Mutlu
ETH Zurich
Spring 2019
14 May 2019